## Slide 1: Digital twin for wind energy industry
Adrien Hirvoas, Ph.D. - FEM
ISEN Yncréa Ouest

## Slide 2: Digital twin for wind energy industry
Day 1: Welcome and Introduction Why wind energy ? Digital Twin Overview Practical work - Python: TP – Python introduction TP – Pandas introduction TP – Anomaly detection introduction | Day 2: Introduction Overview of OpenFAST Practical work: Inputs and outputs workflow Running OpenFAST OpenFAST Modules OpenFAST tool: python-toolbox Practical work: Practicing Run your first simulation | Day 3: OpenFAST reminder OpenFAST tutorial Practical work: Post-Processing A digital twin approach Anomaly detection Conclusion & Question

## Slide 3: Day 3 - Agenda
Introduction
OpenFAST excercise
Conclusion & Question

## Slide 4: Introduction – Digital Twin Goal
Digital Twin - Wind Turbine
What for ?
Improve availability
Reduce operational expenditure (OPEX)
Streamline inspection
Anticipate life extension
Improve future designs

## Slide 5: Introduction – Anomaly detection
Definition of anomaly
  An observation that can be considered significantly outside what is « normal »
  Requires some idea what consitutes « normal »
  That is very much non-trivial
  Statistically: Given input data , an anomaly is a sample with a specific value for its pdf,
  Calculating is also very much non-trivial

## Slide 6: Introduction – Anomaly detection
Expectation: in a healthy system there should be robust relationships between states of components
Example: the motion of a FOWT dominantly deponds on wind speed and other environmental conditions
Therefore, statistical modeling should deliver good predictions of first from the former
Deviations can be explained by defects between numerical model and measure
Environmental inputs
Wind speed & direction
Wave amplitude & direction
Current speed & direction
Atmospheric conditions
Output signals

## Slide 7: Introduction – Anomaly detection
Threshold
Arguably biggest challenge: when is a model/measure deviation « unusual »
Statistical modeling of distribution
Some quantile of modeled distribution taken to be alert threshold

## Slide 8: Introduction – Wind Turbine Post Treatment
Power spectrum density
Visual explanation
Rigid body modes
Tower + platform

## Slide 9: Introduction – Wind Turbine Post Treatment
Power spectrum density
Visual explanation
1 FA/SS

## Slide 10: Day 2 - Agenda
Introduction
OpenFAST exercise
Conclusion & Questions

## Slide 11: Practice – Offshore wind turbine – Google Colab
What is Google Colab?
  Google Colab which stands for Google Colaboratory is a cloud platform
  provided by Google to run Python Notebook’s without need to install
  anything on your local machine.
Features of Google Colab
  Zero Setup Required
  Free GPU Access
  Pre-installed Libraries
Accessing Google Colab
  https://github.com/Ahirvoas/Training-Day3/blob/main/Tutorial_day3.ipynb

## Slide 12: Day 2 - Agenda
Introduction
OpenFAST exercise
Conclusion & Questions